## Slide 1: Light Amplification by Stimulated Emission of Radiation (LASER)
Reference: Fundamentals of Applied Electromagnetics,
by Ulaby, Michielssen and Ravaioli

## Slide 2: LASER versus other light sources (sun, light bulb)
LASER
Monochromatic: single wavelength
Coherent: uniform wavefront
Narrow-beam
Others
Several wavelengths
Incoherent: random phase
Wide-beam

## Slide 3: Atom model
Nucleus (protons and neutrons) and electron cloud
Orbit
  quantized (discrete) energy state that electron occupies
Move from lower to higher (excited) energy state
  caused by supply of energy: heat or intense light
Pumping:
  exciting atoms
  increasing the population of electrons in higher energy states

## Slide 4: Photon emission
Spontaneous: photon in an excited state moves to a lower state
Stimulated: emitted photon interacts with an excited electron (of another atom), causing it to drop to a lower energy level
Creates a new photon with identical phase, frequency, polarization, and direction

## Slide 5: Operation principle
Flash tube: light excites the atoms, spontaneous emission, generated photons cause stimulated emission
Perfectly reflecting mirror at one end: photons (moving along the tube) bounce back, generating more stimulated emission (amplification)
Partially reflecting mirror at the other end: photons bounce back, a fraction of them go through the mirror

## Slide 6: Wavelength (color)
Given material has unique energy states
Energy difference between high energy state and low energy state determines the wavelength
Bands:
  Ultraviolet: 400 nm (790 THz) to 10 nm (30 PHz)
  Visible: 700 nm (430 THz) to 400 nm (790 THz)
  Infrared: 1 mm (300 GHz) to 700 nm (430 THz)
  Microwave: 1 meter (300 MHz) to 1 mm(300 GHz)