## Slide 1
Chapter 15
Cognitive Radio Networks

## Slide 2: What is a cognitive radio?
Software Defined Radio (SDR)
  Hardware : antenna, preselector, power amplifier, ADC, DAC, computer
  Software : filters, (de)modulators, user interface
Artificial Intelligence (AI)
  Mimicking human thinking with machines
SDR + AI
  Radio senses channel conditions, understands operator's preferences, use past experience, determine operation parameters

## Slide 3
Why smart radio networks?

## Slide 6: The Spectrum Crunch Problem
Global Mobile Data Traffic, 2014 to 2019
Overall mobile data traffic is expected to grow to 24.3 exabytes per month by 2019,
nearly a tenfold increase over 2014. Mobile data traffic will grow at a rate
of 57 percent from 2014 to 2019.
Source: Cisco VNI Mobile, 2015

## Slide 7: Spectrum Crunch (cont'd)
High-End Devices Significantly Multiply Traffic
Source: Cisco VNI Mobile, 2015

## Slide 8: Comparison of Global Device Unit Growth and Global Mobile Data Traffic Growth 2014–2019
Device Type | Growth in Devices | Growth in Mobile Data Traffic
Smartphone | 16.7% | 60.1%
Tablet | 32.0% | 83.4%
Laptop | 5.3% | 22.3%
M2M Module | 45.5% | 102.7%
Machine-to-machine (M2M) connections: home and office security and
automation, smart metering and utilities, maintenance, building automation,
automotive, healthcare and consumer electronics.
Source: Cisco VNI Mobile, 2015

## Slide 9
But...over 80% of spectrum is unused

## Slide 11: Cognitive Radio
More efficient use of radio spectrum
Support of the expected growth of wireless trafic
SDR+AI : smart radios that can use radio spectrum smartly

## Slide 12: Examples
Opportunistic spectrum usage of television white space
Interference temperature for interference control

## Slide 13: Opportunistic Spectrum Usage

## Slide 14: Opportunistic Spectrum Usage

## Slide 15: Opportunistic Spectrum Usage

## Slide 16: WhiteFi (802.11af)
Uses spectrum previously occupied by analog TV channels
Rates 1.5 to 3.1 Mbps
Municipal functions : surveillance cameras, transmitting water quality data
VHF frequencies from 174 to 216 MHz (TV channels 7-13),
UHF frequencies from 470–698 MHz (TV channels 14-52), and
unlicensed frequencies from 902 to 928 MHz

## Slide 17: Super Wi-Fi (802.22)
Wireless Regional Area Net
Use cognitive radio and TV white space (54-862 MHz) to provide broadband to low-population-density areas
Range 30 km, PSK, QAM, OFDM, 1.5 Mbps (downstream), 384 Kbps (upstream), BW 6, 7 or 8 MHz

## Slide 18: Where is the white space?
The database approach!
Secondary users query a DB (via Internet) to find available channels
Secondary users provide their geographic location
Projects : IETF Protocol to Access White Space DB (PAWS); Microsoft, Google White Space DB
The spectrum sensing approach!
Observe the spectrum
Identify non occupied channels

## Slide 19: How to control interference?
Current approach
  power limit on individual transmitters
Others
  Interference temperature approach: a maximum on the cumulative energy from the transmitters
  ...

## Slide 20
Interference
Temperature

## Slide 21: Interference Temperature
Data rate R is proportional to
  Power of primary transmitter
...but inversely proportional to
  Noise
  Interference from secondary transmitter

## Slide 22: Interference Temperature (cont'd)

## Slide 23: Interference Temperature (cont'd)

## Slide 24: Interference Temperature (cont'd)

## Slide 25: Interference Temperature (cont'd)

## Slide 26: Interference Temperature (cont'd)
Limitation
  Current model doesn't take into account receiver's sensitivity